Captured with Wireshark:

Frame 272: 37 bytes on wire (296 bits), 37 bytes captured (296 bits) on interface 0
Bluetooth
Bluetooth HCI H4
Bluetooth HCI Event - LE Meta
    Event Code: LE Meta (0x3e)
    Parameter Total Length: 34
    Sub Event: LE Advertising Report (0x02)
    Num Reports: 1
    Event Type: Scannable Undirected Advertising (0x02)
    Peer Address Type: Random Device Address (0x01)
    BD_ADDR: fb:e1:23:6b:2b:9f (fb:e1:23:6b:2b:9f)
    Data Length: 22
    Advertising Data
        Manufacturer Specific
        Length: 21
        Type: Manufacturer Specific (0xff)
        Company ID: Unknown (0x0822)
        Data: 06040a98bfaf41060a0a9026c9420303008d
        [Expert Info (Note/Undecoded): Undecoded]
    RSSI: -65dBm

from a simple scan program:

Address(string="fb:e1:23:6b:2b:9f") <Advertisement >
Advertisement(data=b"\x15\xff\x22\x08\x06\x04\x0a\x30\xcd\xb2\x41\x06\x0a\x0a\x70\x30\xc9\x42\x03\x03\x00\xcf")

hex dump:

0000 04 3e 22 02 01 02 01 9f 2b 6b 23 e1 fb 16 15 ff .>".....+k#áû..ÿ
0010 22 08 06 04 0a 00 96 b3 41 06 0a 0a 64 32 c9 42 "......³A...d2ÉB
0020 03 03 00 d6 c7 ...ÖÇ

note: the second line has the company ID in a byte swapped format. The xff at the end of the first line (xff) indicates company data. The x04 x0a in the second line is the code for temperature. The preceding x06 is the length of the first data block including the code for type. The next x06 is the length of the next data blob and x0a x0a is the code for pressure.
Note 2: in the advertisement data the x15 is the total length of the remaining data blob.

So. in order to get this to work I could have changed the Adafruit code but chose to break it down myself. All the codes in the Adafruit_ble_broadcastnet.py are byte swaped.

The msmts.py contains a dict with the codes as received. I used a hard coded list of mac address in a list in the secrets.py file to capture the packets from my Clue ( the list is to allow for more sensors). I then check for the xff byte (manufacture data) then strip out the sensor type and data.

Note: when using Wireshark you have to start something to get it to capture anything. I used bleak_scan.py to verify then ran my script to capture the data.